OpenGL Basics

---
What is OpenGL?
- OpenGL is a software specification. It acts as a layer between our program and graphics driver.
- OpenGL is implemented as a software interface(API) that allows the programmer to create 2D and 3D graphics images.

---
Why OpenGL?
- Device independence
- Platform independence
  - SGI Irix, Linux, Windows
- Abstractions (GL, GLU, GLUT)
- Open source
- Hardware-independent software interface
- Support of client-server protocol
- Other APIs
  - OpenInventor (object-oriented toolkit)
  - DirectX (Microsoft)
  - Java3D (Sun)

---
Modes of operation/design:
- Immediate mode: draw calls directly render to screen.
- Retained mode: draw calls fill a buffer(abstract data model) and OpenGL decide when to render.
- We’ll be dealing with immediate mode.

---
Immediate mode pipeline:

---
Primitives
- Supports several basic primitives such as points, lines, triangles, quadrilaterals and general polygons.
- Primitives are specified using a sequence of vertices.
- Syntax:
- glBegin(<primitive type>);
  glVertex2f(x0,y0);
  glVertex2f(x1,y1);
  .
  .
  glEnd();
- Where x0, y0, x1, y1 ... are variables of GLfloat type.

---
Primitive types:
The numbers indicate the order in which the vertices have been specified.

---
Colours in OpenGL
- Colors are specified in RGB/RGBA mode. Values of [0...1] or [0...225] are acceptable depending on the function called.
- Function used: glColor();
- Function format: glColor[data type nemonic]();
- glColor() has different forms depending upon the color values you want to specify.
  - For eg.:
  - glColor3f(0.0f, 1.0f, 0.0f);	// sets green color using GLfloat.
  - glColor3ui(255,0,0);	// sets color to red using GLuint.
  - glColor4f(1.0f, 0.0f, 0.0f, 1.0f);	// sets color to red using GLfloat and sets alpha value to max.
  - glColor3fv(cv);	// sets color based on cv of type GLfloat *.

---
Coordinate system in OpenGL
- Different coordinates are used to make calculations easier.
- OpenGL expects coordinates to be in Normalised Device Coordinates(NDC) range -1 to 1.
- Models are defined based on their local origin.

---
Model Matrix
- Local coordinates are relative to its local origin at (0,0,0).
- The model matrix transforms a position in a model to the position in the world by combining translation, scale and rotation.

---
View / Camera matrix
- View space coordinates are relative to the viewer(camera or eye view).
- This matrix transforms the objects/vertices to mimic a camera/observer location.

---
Projection matrix
- It is used to create a viewing box/frustum that defines what should be visible and what should be clipped based on view-space coordinates.
- All the coordinates outside this frustum after transforming them to clip space get clipped.
- Projection matrix transforms the coordinates to normalised device coordinates(NDC) [-1...1].
- Projection matrices are of two types:
  - Perspective: objects farther away look smaller
  - Orthographic: objects are not affected.

---
MVP matrix
- MVP matrix: Model View Projection Matrix is a transformation matrix that is used to convert local coordinated to clip coordinates.
- Vclip = Mproj·Mview·Mmodel·Vlocal

---
Coordinate system in OpenGL

---
Going 3D
- 3D graphics use the concept of MVP matrix, Lighting, shading, textures etc. to convert 3 dimensional vertices into 2D pixels.
- We’ll see 2d & 3d examples later.

---
- Windows setup – Sayli Patil
- Glut introduction & setup – Abhishek Gawade
- Linux setup & demos – Mukesh Tandale